## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch

## Slide 2
Progress Updates
Cleaned up the SoftHier simulator Git repository
  Developed a new build process for non-Eth machines
  Prepared a simple tutorial
    Get started with SoftHier Simulation
    Architecture and configuration files
    Example of SW for SoftHier
      Use DMA to transfer data: HBM <-> cluster; cluster <-> cluster
      Use RedMule to accelerate GEMM in cluster L1
      Inter-/intra-cluster synchronization
  Still need to provide toolchains to build SW
https://github.com/gvsoc/gvsoc/tree/soft_hier_flex_cluster

## Slide 3
General MatMul Kernel for SoftHier
MatMul Kernel SW
  Program Cluster to behave like Systolic array
  Tiling policy:
    best usage of Cluster L1 capacity
  Mapping policy:
    enable clusters according to tiles on M and K dimensions
W00
W01
W10
W11
W20
W21
W30
W31
I00
I01
I10
I11
I02
I03
I12
I13
I20
I21
I22
I23
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
M
N
N
K

## Slide 4
Performance
SoftHier config
  4x4 Cluster(128x32 RedMule)
  NoC Link BW: 512bit
  HBM: 8 channel, 512 GB/s
  Peak Perf: 128TFLOPS
Evaluation:
  Different M-N-K of MatMul
  Tile size = 256
Result:
  M,K determines how many clusters are enabled
  Large N helps to reach high compute utilization
  Jagged curve due to leftover tiles on M & K dimension
N=256
N=1024
N=4096
N=16384
M=K=256, only one cluster is enabled for computation
N=16384, M & K increase from 2048

## Slide 5
Collaboration Plan
Master Thesis: Automative GEMM Kernel deployment framework for SoftHier architecture
  Basic goal:
    Complete the SoftHier Backend in DaCe: SDFG -> executable SoftHier code
    Evaluate GEMM performance on SoftHier with baseline DaCe SDFG transformation (GPU Frontend, local shared memory + DMA, no inter-cluster data communication/hard-coded schedule)
    Compare to hand-written optimized GEMM kernel performance
  Stretch goals:
    Extend DaCe frontend to support inter-cluster data communication
    Discussion on tiling, mapping and scheduling schemes in SDFG transformation.

## Slide 6
Next Steps
Baseline end-to-end LLM on SoftHier
  Code for rest kernels in LLM: softmax, normalization.
  Support Matrix Transposition in RedMule: required by attention head
  Evaluate end-to-end performance of LLM inference: prefill & decode

## Slide 7: SoftHier Progress Update
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 8
Status
Thomas was away for 4.5 weeks due to military service and just resumed work last Thursday.

## Slide 9: SoftHier Progress Update
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 10
Snitch cluster updates
Primarily busy on multicast paper (submitted to AICAS)
  Extended Snitch cluster, iDMA and Occamy interconnect with multicast support
  Evaluated the benefit of multicast for ML workloads, benchmarking GEMM kernel improvements
  Potentially useful insights for SoftHier project
Merged PRs
  #192: significant improvements to Docker container and CI execution time
  #175: update tool dependencies
  #184: improve error messages on illegal instruction and misaligned load/stores