## Slide 1: FlatAttention: Dataflow and Fabric Collectives Co-Optimization for Efficient Multi-Head Attention on Tile-Based Many-PE Accelerators
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Colagrande, Renzo Andri, Thomas Benz, Gamze Islamoglu, Alessandro Nadalini, Francesco Conti, Yawei Li and Luca Benini

## Slide 2
The Attention Bottleneck in Transformer-Based LLMs
LLM workloads have become increasingly impactful
  DeepSeek-V3, ChatGPT, Llama
Dominating LLM are Transformer-based
The attention bottleneck
  Multi-Head Attention (MHA) exhibits quadratic complexity over sequence length. O(S2)
  Most operations in MHA are bottlenecked by memory accesses[1]
  Performance bottleneck for
    LLM inference
      Especially during long context prefill
    LLM training
Q
Attention Score
KT
D
S
S
O
SoftMax(Att.Score)
S
V
(1).
(2).
(3).
Multi Heads

## Slide 3
SoA Solution: FlashAttention-3 on Nvidia H100 GPU
The attention bottleneck has driven optimizing MHA dataflows on the dominant AI hardware platform – Nvidia GPU
FlashAttention[2] – most widely adopted solution
  Efficiently fuses MHA microkernels
  FlashAttention-2[8]: algorithmic optimizations
  FlashAttention-3[9]: leverages asynchronous execution
Drawback of SoA solution: FlashAttention-3 on H100
  Suboptimal performance
    No more than 75% utilization on H100
  High cost of hardware platform
    814 mm2 die on TSMC’s 5nm process node
    6 HBM3 stacks – up to 50% total cost
    700W Thermal Design Power(TDP)
HBM
HBM
HBM
HBM
HBM
HBM
Die

## Slide 4
Emerging AI Accelerator: Tile-Based Many-PE Architecture
Tile-based many-PE accelerators
  Structured as meshes of compute tiles
    Extremely dense matrix, vector and scalar engines
    Local explicitly managed memories
  Interconnect with scalable NoC topology
  Main memory positioned at die boundaries
Favors silicon efficiency and scalability
  A dense compute tile placement
  Software-controlled partitioned memory hierarchy
  Eliminates L2 on-chip cache for area efficiency
Examples
  Tesla’s Dojo, Tenstorrent’s Blackhole, SambaNova
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
HBM CTRL
CH0
CH1
…
CHn
I$
Matrix engine
L1 local memory
DMA
Scalar core
Vector engine
interconnect
To Router
SM
HBM CTRL
HBM CTRL
HBM CTRL
L2 Cache
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
SM
L1
HBM CTRL
HBM CTRL
HBM CTRL
Tile-Based Many-PE
vs Nvidia GPU Arch

## Slide 5
Challenge: MHA Dataflow on Tile-Based Many-PE Architecture
The goal is to
  Achieve high utilization of the tiles’ matrix engines
  Minimize energy-hungry off-chip accesses
Current solutions
  have not reached > 80% utilization on PetaFLOPS chips.
Architecture and dataflow need to be co-explored
  Dataflow leverages HW feature, e.g., collective primitives on NoC fabric
    Accelerate inter-tile collective communications
  Determine optimal architecture design parameters alongside dataflow exploration
SW-Based Multicast
(1)
(2)
(3)
HW-Supported Multicast
Packet Duplicate & Forward

## Slide 6
Our Contributions
SoftHier – modeling and simulation framework
  Estimating the performance of a large set of tile-based accelerators
  Enabling the co-design of network collective primitives
FlatAttention MHA dataflow
  Leverages collective primitives on the NoC fabric and minimizes off-chip HBM traffic
  Co-exploration of accelerator architecture and FlatAttention parameters
Key Results
  FlatAttention vs. FlashAttention-3 on tile-based accelerator
    Up to 89.3% utilization, 4.1× performance speedup, 16× HBM traffic reduction
  Algorithm-architecture co-exploration -> find optimal configuration of tile-based accelerator (BestArch)
    Peak FP16 Perf(1024 TFLOPS) matches H100 (989 TFLOPS)
    40% less available HBM BW, 1.8× die size reduction (estimated at TSMC 5nm)
    Up to 1.3× utilization speedup (FlatAttention on BestArch vs. FlashAttention-3 on H100)

## Slide 7
FlatAttention Motivation
Analysis start from FlashAttention
  Fuse microkernels of each head attention
  MHA workload is partitioned to tiles over:
    Batch size, number of heads, output sequence dimension
  Every tile processes independently
    Every tile need to access in HBM
    No communication between tiles is required
  Results in an HBM I/O complexity of
    Sequence length S, head dimension D, number of heads H, batch size B and block size M:=Br=Bc
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Q: S x d
KT: d x S
V: S x d
d x Bc
Br x d
Bc x d
Copy Block to SRAM
Copy
Copy
Inner Loop
Inner Loop
Outer Loop
Outer Loop
Output to HBM
sm(QKT)V: S x d
Br x Bc

## Slide 8
FlatAttention Motivation
FlatAttention – Redefine how MHA is parallelized
  Leverages multiple tiles as a unified entity
  Process an MHA block of a significantly larger size
    The aggregate L1 memory of a group of tiles
    Collectively store the block
  When N tiles are grouped together, HBM I/O complexity:
  More tiles are grouped, less HBM accesses needed
Q: S x d
KT: d x S
V: S x d
d x Bc
Br x d
Br x Bc
Bc x d
Copy Block to SRAM
Copy
Copy
Inner Loop
Inner Loop
Outer Loop
Outer Loop
Output to HBM
sm(QKT)V: S x d
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile

## Slide 9
Detailed FlatAttention Dataflow
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
Tile
KT
O
Q
Attention Score
Gy
V
Bc
Bc/Gx
Gx
Bc
Bc/Gx
Br
Br/Gy
Distinct data movement patterns within the tile group
  Edge tiles collect data from HBM once and inter-tile data exchange via collective communications
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
Load Q and row-wise multicast
V
V
V
V
1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
m l e l-1 m-1
O
Att
KT
Q
O
Att
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Load KT V and col-wise multicast
V
V
V
V
2
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
O
S
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate att.score, scaling, and local rowmax m
V
V
V
V
3
m l e l-1 m-1
m l e l-1 m-1
Row-wise red.max m and multicast
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
m l e l-1 m-1
O
S
KT
Q
O
S
KT
Q
m l e l-1 m-1
m l e l-1 m-1
V
V
V
V
4
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate softmax numerator P and demoninator l
V
V
V
V
5
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Row-wise red.sum l and multicast
V
V
V
V
6
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
m l e l-1 m-1
m l e l-1 m-1
Calculate and update local O & tracking statistics l-1 , m-1
V
V
V
V
7
m l e l-1 m-1
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
m l e l-1 m-1
O
P
KT
Q
O
P
KT
Q
Finalize O with demoninator , row-wise red.sum and store back to HBM
m l e l-1 m-1
m l e l-1 m-1
V
V
V
V
8

## Slide 10
Asynchronous FlatAttention
To further improve utilization
  Using asynchronization nature of {DMA, Matrix, Vector} engines invoking
  One tile group dealing with 2 heads concurrently
  Overlap the runtime of {DMA, Matrix, Vector} engines
O
Att
KT
Q
m l e l-1 m-1
Naïve FlatAttention
x1
V
DMA
Matrix
Engine
Vector
Engine
O
Att
KT
Q
m l e l-1 m-1
x2
V
Asynchronous FlatAttention
DMA
Matrix
Engine
Vector
Engine

## Slide 11
High-Level Simulation Model – SoftHier System
Fully Parameterizable through Configuration File
  System configuration
    #Tiles (#row, #column)
    NoC link data width
    #HBM channels and placement on 4 edges
  Cluster configuration
    L1 memory capacity and bandwidth
    Matrix engine systolic array (shape, CE pipeline stage)
    DMA burst length, #outstanding burst
Based on GVSoC[10] Platform
  Event-based simulator, fast simulation speed up to 25 MIPS
Calibrated with RTL Models
https://github.com/gvsoc/gvsoc/tree/soft_hier_release
Core 0
Core 0
…
Core n
Matrix
Engine
DMA
I $
L1 local memory
Vector
Engine
Interconnect
To DATA NoC Router
To SYNC NoC Router
TE Cluster
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router

## Slide 12
FlashAttention vs. FlatAttention
Compare different MHA implementations
  FlashAttention-2(FA-2) and FlashAttention-3 (FA-3)
  Naïve FlatAttention without (Flat) and with (FlatColl) Collective primitves on NoC fabric.
  Asynchronous FlatAttention (FlatAsyn) with NoC collective primitives
With FlatAttention group includes all tiles
Results
  FlashAttention is highly memory-bound
  FlatAttention significantly reduces HBM access
  NoC supported collective primitives are essential to accelerate inter-tile data exchange
  With NoC collective primitives + Asynchronous:
    Up to 89.3% uti, 4.1× perf speedup, 16× less HBM traffic

## Slide 13
Tile Group ScaleTrade-offs for FlatAttention
The group scale is a sensitive parameter to utilization of different MHA layers
  MHA with long sequences benefit from large tile group
    Reduced overall HBM traffic
  MHA with shorter sequence length would suffer from “over-flatten effect”.
    Reduced slice size per tile
    Reduced matrix engine utilization
    Increased synchronization overhead
  For every sequence length there exists an optimal group scale balancing the two effects
Tile
Tile
Tile
Tile
O
Att
KT
Q
m l e l-1 m-1
V
slice size per tile

## Slide 14
Co-exploration of Architecture and Algorithm Parameters
Our goal
  Design a tile-based accelerator with comparable peak performance to Nvidia’s H100
  While improve utilization and reducing overall HBM bandwidth requirements on MHA workloads
Searching for both architecture and MHA dataflow parameter design space
  Select BestArch for performance over cost
  Up to 1.3× utilization speedup in MHA (FlatAttention on BestArch vs. FlashAttention-3 on H100)
  Up to 1.2× utilization speedup in GEMM (SUMMA on BestArch vs. Torch.Matmul on H100)
  Require 40% less available HBM BW to H100
Estimate die area cost from reference RTLs
  1.8x die size reduction to H100 (TSMC 5nm)

## Slide 15
Conclusion For FlatAttention
We propose FlatAttention
  An optimized dataflow for MHA on tile-based many-PE accelerators
  Co-designed with NoC collective primitives
  FlatAttention vs. FlashAttention-3 on tile-based accelerator
  Up to 89.3% utilization, 4.1× performance speedup, 16x HBM traffic reduction
Through algorithm architecture co-exploration
  Find optimal configuration of tile-based accelerator (BestArch)
  Peak FP16 Perf(1024 TFLOPS) Match H100 (989 TFLOPS)
  40% less available HBM BW, 1.8× die size reduction (estimated at TSMC 5nm)
  Up to 1.3× utilization speedup in MHA (FlatAttention on BestArch vs. FlashAttention-3 on H100)
  Up to 1.2× utilization speedup in GEMM (SUMMA on BestArch vs. Torch.Matmul on H100)

## Slide 16
Beyond FlatAttention: Work in Progress
End-to-End Deployment of SoA Models
  Emphasis on full-stack implementation (e.g., DeepSeek)
  Support for low-compute operators essential for complete End-to-End flows
  Focus on workloads in non-prefill inference
    Toward autoregressive and reasoning-heavy strategies
    Methods like beam search becoming increasingly relevant
Automatic code generation for optimal dataflow
  SoftHier backed in DaCe[12] (Data-Centric Optimization) framework for automated code generation, in collaboration with Prof. Torsten Hoefler’s group.
  Automating design space exploration for both architecture and dataflow
  E.g., for GEMM, this tool flow helps us find better HW-SW solutions that outperform DeepGEMM on H100
SoftHier Framework
Tiling
Parameter
Data
Layout
Workload
Maping
Dataflow
Design Space
Co-exploration

## Slide 17
References
[1] A. Ivanov et al., “Data movement is all you need: A case study on optimizing transformers,” in MLSys, 2021.
[2] T. Dao et al., “FlashAttention: Fast and memory-efficient exact attention with IO-awareness,” in NeurIPS, 2022.
[3] F. Zaruba et al., “Snitch: A tiny pseudo dual-issue processor for area and energy efficient execution of floating-point intensive workloads,” IEEE TCOMP, 2020.
[4] T. Benz et al., “A high-performance, energy-efficient modular DMA engine architecture,” IEEE TCOMP, 2023.
[5] T. Fischer et al., “FlooNoC: A 645-Gb/s/link 0.15-pJ/B/hop open-source NoC with wide physical links and end-to-end AXI4 parallel multistream support,” IEEE TVLSI, 2025.
[6] Y. Tortorella et al., “RedMule: A mixed-precision matrix–matrix operation engine for flexible and energy-efficient on-chip linear algebra and TinyML training acceleration," FGCS, 2023.
[7] M. Perotti et al., “Spatz: Clustering compact RISC-V-based vector units to maximize computing efficiency,” IEEE TCAD, 2025.
[8] T. Dao, “FlashAttention-2: Faster attention with better parallelism and work partitioning,” in ICLR, 2024.
[9] J. Shah et al., “FlashAttention-3: Fast and accurate attention with asynchrony and low-precision,” in NeurIPS, 2024.
[10] N. Bruschi et al., “GVSoC: a highly configurable, fast and accurate full-platform simulator for RISC-V based IoT processors,” in ICCD, 2021.
[11] D. Schor, “TSMC N3, and challenges ahead,” 2023. [Online]. Available: https://fuse.wikichip.org/news/7375/tsmc-n3-and-challenges-ahead/
[12] Rausch, Oliver, et al. "A data-centric optimization framework for machine learning." in SC, 2022.