## Slide 1: QuantSparse 3D Biweekly 2025-04-08
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  Spatz: GVSoC Modeling and RTL
  NoC packing: GVSoC Modeling
  3D stacking: Literature Review and Initial Plan
Timeline
Discussion

## Slide 3: Spatz GVSoC Model Update
Original Spatz model in SoftHier
  Configurable number of VLSU ports
  Configurable L1 bank data width
  Fixed VLSU bus-width

## Slide 4: Spatz GVSoC Model Update
Original Spatz model in SoftHier
  Configurable number of VLSU ports
  Configurable L1 bank data width
  Fixed VLSU bus-width
Updated Spatz model
  Configurable VLSU bus-width
  Updated vector instruction libraries
    Vector load: vleX.v (X=8, 16, 32, 64)
    Vector store: vseX.v (X=8, 16, 32, 64)
Additional instruction support
  Minor fix on vid.v
https://github.com/gvsoc/gvsoc/tree/soft_hier_release(#94, #99)

## Slide 5: Spatz N:M Structure Sparsity RTL Update
Spatz has a limited stride/index load support
  64-bit stride load/store operations are supported
  Lower precision stride load/store operations are missing
  Index load/store operations are missing
Current progress
  The student project started working on low-precision stride load/store RTL implementation
https://github.com/gvsoc/gvsoc/tree/soft_hier_release(#94, #99)

## Slide 6: NoC Packing Scheme: Cluster (TX) side
Started work on cluster-side (TX) architecture design
  Wide bus (e.g. 256b) split into narrow request lanes (e.g. 64b)
  Parallel address generators generate strided or indirect sequences
    Determine target NoC endpoint
    Indices fetched from L1
  Per-lane reorder buffers store reqs, vote to decide next target endpoint
    Goal: maximum BW utilization
  Request sequences are segmented, limiting latency and preventing starvation
TX Packer
segment control
endp. vote
L0 ROB
BM
CAM
L1 ROB
BM
CAM
L2 ROB
BM
CAM
L3 ROB
BM
CAM
endps
ctrl
flit hdr.
flit data
Req. Gen
narrow addrgen
segment control
narrow addrgen
narrow addrgen
narrow addrgen
DMA xfers (strided/indir)
Index fetch (to TCDM)
narrow requests
Segment: (ID, R/W,
#reqs)
ctrl

## Slide 7: NoC Packing Scheme: GVSoC Implementation
Worked on implementation of TX model in GVSoC
Common requirement: FIFO buffers with backpressure support
  Existing GVSoC queues enqueue callback times on push  complex handling required in case of stalls
  Alternative: Recurring callback on head whenever nonempty  No downstream stall handling!
Worked on reusable dataflow FIFO for simpler backpressure
No reschedule on stall; just disable evt. when empty
Store data, enable recurring event if off
Data3
Data2
Data1
Data0
Recurring FIFO evt. (data is at head)
Dataflow FIFO
On stall: must reschedule
pending events!
Store data, enqueue event
at t + fill
Data3
evt @ t+3
Data2
evt @ t+2
Data1
evt @ t+1
Data0
evt @ t
GVSoC Queue

## Slide 8: 3D-Chiplet Integration: Literature Review
IntAct[1]: Architecture overview
  Six 16-core chiplets in 28nm FDSOI technology
  3D-stacked onto a 65nm CMOS active interposer
  Active interposer is not just wiring:
    Integrated power management
    Distributed NoC for chiplet-to-chiplet communication
    System I/O PHYs
Face-to-face 3D stacking
  20 µm-pitch micro-bumps3 Tbit/s/mm² bandwidth density
  Distributed Interconnects via Active Interposer  Hierarchical NoC: 2D NoCs inside chiplets + 2D NoC in the interposer

## Slide 9: 3D-Chiplet Integration: Initial Plan
Current SoftHier Clusters
  PEs clustered in 2D NoC mesh, HBM as main memory
  NoC enables:
    Cluster L1  HBM, Cluster L1  Cluster L1
  Wide link data NoC, iDMA for buck data transfer
  Narrow link sync NoC, snitch core remote access for global synchronization purposes

## Slide 10: 3D-Chiplet Integration: Initial Plan
Current SoftHier Clusters
  PEs clustered in 2D NoC mesh, HBM as main memory
  NoC enables:
    Cluster L1  HBM, Cluster L1  Cluster L1
  Wide link data NoC, iDMA for buck data transfer
  Narrow link sync NoC, snitch core remote access for global synchronization purposes
  Initial plan:
  Extend the GVSoC data router model with two additional degrees of freedom
  Literature review on physical feasibility, design specifications, and advancements in chiplet-based 3D integration technologies

## Slide 11: Timeline
2025-02
Literature
Review
2026-02
2027-02
Project
Start
Year 1
Year 2
  Literature review on sparsity and quantization format supported on SoA platforms
  Proposed Spatz-based multi-cluster architecture
  Literature review on quantization handling
  Multi-granularity sparsity handling
  Spatz GVSoC model VLSU port extension
  Start GVSoC modeling of NoC packing scheme
  Initial discussion on 3D chiplet integration
2025-04

## Slide 12: Timeline
2025-02
Literature
Review
2026-02
2027-02
Project
Start
Year 1
Year 2
  Literature review on sparsity and quantization format supported on SoA platforms
  Proposed Spatz-based multi-cluster architecture
  Literature review on quantization handling
  Multi-granularity sparsity handling
  Spatz GVSoC model VLSU port extension
  Start GVSoC modeling of NoC packing scheme
  Initial discussion on 3D chiplet integration
2025-04
  Customized data format for MX-like quantization and N:M structured sparsity
  Customized ISA support in Spatz GVSoC model
  Literature review on 3D chiplet integration and discussion on GVSoC modeling
  Next step:

## Slide 13: References
[1] Vivet, Pascal, et al. "IntAct: A 96-core processor with six chiplets 3D-stacked on an active interposer with distributed interconnects and integrated power management." IEEE Journal of Solid-State Circuits 56.1 (2020): 79-97.