## Slide 1: SoftHier Bi-Weekly Meeting
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 2
SoftHier Progress General Updates
Chi comes back from holiday recently
Some work did before holiday
  We started to prepare the final report for SoftHier project
  We also plan to extend the FlatAttention work to journal extension
    Including the exploration we did: DeepSeek on SoftHier, the FlatMLA implementation
  We received the MoE distribution dataset from your side and started model dedicated Network-on-Interposer
    Detailed modeling of D2DLink
    Extend Router model with other topologies: HexaMesh, OctaMesh, FoldedTorus, etc

## Slide 3
DeepSeekv3 FP8 Decoding on SoftHier
SoftHier Chip Configuration
  Each cluster with one 32x32 CE array RedMule (2TFLOPs/cluster)
  32x32 cluster with total 2048 TFLOPs @FP8
  32 HBM2.ch on both west and south die boundary (4TB/s)
Expert-Parallelism
  Each chip handles a subset of experts in parallel
  Requires heavy inter-chip communication (dispatch & combine)
  Overlaps communication with kernel execution
  Configure with EP-64
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 63
……
C2C Interconnect
Expert 0
Expert 1
Expert 2
Expert 3
Expert 4
Expert 5
Expert 6
Expert 7
Expert 8
Expert 9
Expert 10
Expert 11
Expert 252
Expert 253
Expert 254
Expert 255
Time
C2C Communication
Kernel Compute
MLA + Shared Expert + Gate
MLA + Shared Expert + Gate
Routed Expert
Routed Expert
Dispatch
Dispatch
Combine
Combine
MLA + Shared Expert + Gate

## Slide 4
Previous Analyse Network-on-Interposer with GVSoC NoC Model
Motivation
  C2C communication need to overlap with kernel computation
  Supposing we connect chips with on-chip routers on active interposer, with a 2D Mesh
  Analyse the link BW required
Drawback
  Not using the real DeepSeek MoE distribution
  D2DLink has different characteristics than link in a NoC
    Very long latency, >200ns
    Normally use credit-based flow control
  Need to discuss with more topologies rather than 2D Mesh
R
R
R
R
R
R
R
R
R
Active Interposer
SoftHier
Chip 0
SoftHier
Chip 1
SoftHier
Chip 2
SoftHier
Chip 3
SoftHier
Chip 4
SoftHier
Chip 5
SoftHier
Chip 6
SoftHier
Chip 7
SoftHier
Chip 8
Ideal BW Uti%
Generate Expert Activation Distribution Examples

## Slide 5
DeepSeek MoE – Expert Activation Distribution
Pretty thanks for your help!
  We manage to open and analyse the DeepSeek’s MoE experts' activation distribution for each layer
  Questions:
    We got the bincounts data for expert activation, are experts sorted according to their counts?

## Slide 6
We Model the D2DLink in GVSoC
D2DLink Model
  Higher abstraction for serial link IP we developed
  Credit-based flow control
  Long latency configurable
RX
TX
RX
TX
Abstraction
latency
latency

## Slide 7
We Model the D2DLink in GVSoC
D2DLink Model
  Higher abstraction for serial link IP we developed
  Credit-based flow control
  Long latency configurable
RX
TX
RX
TX
RX
TX
RX
TX
8
8
8
8
latency
latency

## Slide 8
D2DLink GVSoC Model Characteristics
D2DLink Model
  We have the D2DLink GVSoC model ready
  Benchmark the characteristics:
    Packet Size = 256Byte
    Credit Buffer Size = 512 packets
RX
TX
RX
TX
latency
latency
Chart: Throughput vs Transfer Size (link latency = 256ns)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
16GBps | 3.34 | 5.52 | 8.21 | 10.85 | 12.93 | 14.3 | 15.1 | 15.54 | 15.77 | 15.88 | 15.94
32GBps | 3.62 | 6.5 | 10.81 | 16.16 | 21.47 | 25.7 | 28.51 | 30.15 | 31.05 | 31.52 | 31.76
64GBps | 3.78 | 7.14 | 12.84 | 21.39 | 32.06 | 42.72 | 51.24 | 56.91 | 60.25 | 62.07 | 63.02
128GBps | 3.86 | 7.5 | 14.17 | 25.52 | 42.56 | 63.88 | 85.22 | 102.32 | 113.73 | 120.44 | 124.11
256GBps | 3.91 | 7.7 | 14.95 | 28.25 | 50.88 | 84.89 | 127.5 | 170.22 | 201.34 | 223.48 | 236.49
Chart: Credit Depletion
| 100 | 200 | 300 | 400 | 500 | 600 | 700
128GBps | 126.44 | 124.93 | 123.46 | 122.03 | 120.62 | 101.28 | 87
256GBps | 249.78 | 243.97 | 202.35 | 152.37 | 122.18 | 101.98 | 87.51
Chart: Throughput vs Transfer Size (Link BW = 256GBps)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024
Link Latency =16ns | 46.55 | 78.77 | 120.47 | 163.84 | 199.8 | 224.44 | 239.18 | 247.31 | 251.58 | 253.77 | 254.88
32ns | 26.95 | 48.76 | 81.92 | 124.12 | 167.18 | 202.27 | 225.99 | 240.06 | 247.77 | 251.82 | 253.89
64ns | 14.63 | 27.68 | 49.95 | 83.59 | 126.03 | 168.91 | 203.53 | 226.77 | 240.5 | 248.01 | 251.94
128ns | 7.64 | 14.84 | 28.05 | 50.57 | 84.45 | 127.01 | 169.78 | 204.16 | 227.16 | 240.72 | 248.12
256ns | 3.91 | 7.7 | 14.95 | 28.25 | 50.88 | 84.89 | 127.5 | 170.22 | 201.34 | 223.48 | 236.49

## Slide 9
Router Supporting for more Flexible Topologies
Topologies
  Mesh
  HexaMesh
  OctaMesh
  FoldedTorus
  …
Routing Algorithm
  Dimension-order routing
  Example for OctaMesh
Current Status:
  We have the router implemented in GVSoC
  Now we are setting up experiments for the MoE dispatch & combine test
0
1
2
3
Start

## Slide 10
Plan For Next
Mainly working on the final report and FlatAttention Journal Extensions
Collecting the results for DeepSeek MoE dispatch and combine on a more dedicated Network-on-Interposer GVSoC model