## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 2
Benchmark LLama2 MLP block
Weight
Input
384
256
5120
Sequence length
384
256
13824
5120
Output
13824
Sequence length
384
384
iDMA
x6
iDMA
HBM Channel
x8
HBM Channel
    Max 384GB/s
    HBM2E: Max 410GB/s
iDMA
RedMule
Xbar
TCDM
#Banks = 32
Bank Width = 32b
Total Memory = 1MB
128
GB/s
64GB/s
Problem Size
  Sequence length x 5120 x 13824
    Let the sequence length = 768
Implementation
  Clusters take care of different output tiles (384x384).
  At each round:
    iDMA transfers input matrix tile + weight matrix tile from HBM
    RedMule GEMM 384x256x384.
Variables
  RedMule Configuration:
    48x16 arrays -- 768 MACs/Cycle
    96x32 arrays -- 3072 MACs/Cycle
  Data format: FP8, FP16

## Slide 3
Results
Chart: RedMule-48x16-FP8
| redmule | idma
Busy | 3061119 | 855037
Idle | 0 | 2206082
Sync | 63375 | 63375
Chart: RedMule-48x16-FP16
| redmule | idma
Busy | 3131284 | 1418645
Idle | 0 | 1712639
Sync | 72370 | 72370
Chart: RedMule-96x32-FP8
| redmule | idma
Busy | 867815 | 737971
Idle | 0 | 129844
Sync | 24762 | 24762
Chart: RedMule-96x32-FP16
| redmule | idma
Busy | 938220 | 1418645
Idle | 480425 | 0
Sync | 64407 | 64407
Chart: Utilization
| RedMule-48x16-FP8 | RedMule-48x16-FP16 | RedMule-96x32-FP8 | RedMule-96x32-FP16
RedMule Compute Uti | 0.94387 | 0.92055 | 0.82601 | 0.49714
HBM BW Uti | 0.221 | 0.43109 | 0.77363 | 0.93122
End-to-End System Performance
  Occamy + 48x16 RedMule, 410 GB/s HBM
    FP8: 34.6 TOP/s
    FP16: 34.3 TOP/s
  Occamy + 96x32 RedMule, 410 GB/s HBM
    FP8: 120.9 TOP/s
    FP16: 72.3 TOP/s
BW-Bound When:
    RedMule 96x32
    FP16 GEMM
  But in Roofline Model
    MLP AI = 637 OP/B
    > Roofline Limit 359 OP/B
Improvement:
  Inter-Cluster Data Reuses

## Slide 4
Leverage Inter-Cluster Data Reuses
Modeling
  Previous model only contain Cluster-to-HBM Interconnect
  Modeling Cluster-to-Cluster Interconnect
    Also triggered by iDMA in each Cluster
    Modeling Finished
Current Progress:
  New Code for LLama2 MLP Layer
  Take Inter-Cluster Transfer into account
  We first do intra-quadrant communication only

## Slide 5
HBM
MLP Layer Dataflow: initial stage
Weight
Input
I00
384
256
5120
Sequence length
W00
384
256
13824
5120
Output
13824
Sequence length
O00
384
384
I01
I10
I11
W01
W10
W11
O01
O10
O11
I00
W00
I11
W10
I10
W01
I00W00 + I01W10 = O00_part
I00W01 + I01W11 = O01_part
I10W00 + I11W10 = O10_part
I10W01 + I11W11 = O11_part
I01
W11
I00
W00
I11
W10
I10
W01
I01
W11
Example in one quadrant
  0. Initial stage

## Slide 6
Weight
Input
I00
384
256
5120
Sequence length
W00
384
256
13824
5120
Output
13824
Sequence length
O00
384
384
I01
I10
I11
W01
W10
W11
O01
O10
O11
I00
W00
I01
W11
I11
W10
I10
W01
I00W00 + I01W10 = O00_part
I00W01 + I01W11 = O01_part
I10W00 + I11W10 = O10_part
I10W01 + I11W11 = O11_part
HBM
I00
W00
I01
W11
I11
W10
I10
W01
MLP Layer Dataflow: initial stage
Example in one quadrant
  0. Initial stage
    Load tiles from HBM
    Equally distribute to clusters

## Slide 7
Weight
Input
I00
384
256
5120
Sequence length
W00
384
256
13824
5120
Output
13824
Sequence length
O00
384
384
I01
I10
I11
W01
W10
W11
O01
O10
O11
I00
W00
I01
W11
I11
W10
I10
W01
I00W00 + I01W10 = O00_part
I00W01 + I01W11 = O01_part
I10W00 + I11W10 = O10_part
I10W01 + I11W11 = O11_part
HBM
I00
W00
I01
W11
I11
W10
I10
W01
MLP Layer Dataflow: routines stage
Example in one quadrant
  0. Initial stage
    Load tiles from HBM
    Equally distribute to clusters
  1. Routines stage
    iDMA copy tiles to other clusters

## Slide 8
Weight
Input
I00
384
256
5120
Sequence length
W00
384
256
13824
5120
Output
13824
Sequence length
O00
384
384
I01
I10
I11
W01
W10
W11
O01
O10
O11
I00
W00
I01
W11
I11
W10
I10
W01
I00W00 + I01W10 = O00_part
I00W01 + I01W11 = O01_part
I10W00 + I11W10 = O10_part
I10W01 + I11W11 = O11_part
HBM
I00
W00
I01
W11
I11
W10
I10
W01
O00
O01
O10
O11
MLP Layer Dataflow: routines stage
Example in one quadrant
  0. Initial stage
    Load tiles from HBM
    Equally distribute to clusters
  1. Routines stage
    iDMA copy tiles to other clusters
    RedMule computation

## Slide 9
Weight
Input
I00
384
256
5120
Sequence length
W00
384
256
13824
5120
Output
13824
Sequence length
O00
384
384
I01
I10
I11
W01
W10
W11
O01
O10
O11
I02
W20
I03
W31
I00W00 + I01W10 = O00_part
I00W01 + I01W11 = O01_part
I10W00 + I11W10 = O10_part
I10W01 + I11W11 = O11_part
HBM
I00
W00
I01
W11
I11
W10
I10
W01
O00
O01
O10
O11
I13
W30
I12
W21
MLP Layer Dataflow: routines stage
Example in one quadrant
  0. Initial stage
    Load tiles from HBM
    Equally distribute to clusters
  1. Routines stage
    iDMA copy tiles to other clusters
    RedMule computation
  2. Routines stage
    Load next tiles from HBM
    RedMule computation

## Slide 10
Leverage Inter-Cluster Data Reuses: Results
Chart: RedMule-96x32-FP16-IntraQudrantComm
| redmule | idma
routine1-busy | 459210 | 360990
routine1-idle | 321 | 98541
routine2-busy | 459210 | 709322
routine2-idle | 250233 | 121
Sync | 73345 | 73345
Chart: RedMule-96x32-FP16-NoClusterComm
| redmule | idma
Busy | 938220 | 1418645
Idle | 480425 | 0
Sync | 64407 | 64407
x6
HBM Channel
x8
HBM Channel
    Max 384GB/s
    HBM2E: Max 410GB/s
Results
  Increase RedMule execution uti from 63% to 74%
  Speedup 1.17x …
  Inter-Cluster communication within quadrant is efficient and make kernel compute-bound
  We need more inter-cluster communication phases …
Hierarchical organization is not good for exploring more inter-cluster comm.
  Intra-quadrant BW is sufficient, but inter-quadrant BW is still limited …
  We need another cluster connection topology

## Slide 11
If we move to Mesh NoC topology, how we map MLP
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
I00
384
256
I01
I10
I11
I02
I03
I12
I13
I20
I21
I30
I31
I22
I23
I32
I33
W00
384
256
W01
W10
W11
W02
W03
W12
W13
W20
W21
W30
W31
W22
W23
W32
W33
O00
384
384
O01
O10
O11
O02
O03
O12
O13
O20
O21
O30
O31
O22
O23
O32
O33
x
HBM

## Slide 12
Distribute Tiles to Clusters
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
HBM
I00
I01
I02
I03
I10
I11
I12
I13
I20
I21
I23
I22
I30
I33
I32
I31
W00
W11
W22
W33
W30
W20
W10
W01
W31
W21
W12
W02
W32
W23
W13
W03
  Load All (16 Input tiles, 16 weight tiles) from HBM
  Cluster contain different tiles from each other

## Slide 13
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
I00
I01
I02
I03
I10
I11
I12
I13
I20
I21
I23
I22
I30
I33
I32
I31
W00
W11
W22
W33
W30
W20
W10
W01
W31
W21
W12
W02
W32
W23
W13
W03
HBM
Distribute Tiles to Clusters
  Load All (16 Input tiles, 16 weight tiles) from HBM
  Cluster contain different tiles from each other

## Slide 14
Inter-Cluster Tile Exchanging
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
I00
I01
I02
I03
I10
I11
I12
I13
I20
I21
I23
I22
I30
I33
I32
I31
W00
W11
W22
W33
W30
W20
W10
W01
W31
W21
W12
W02
W32
W23
W13
W03
HBM

## Slide 15
Inter-Cluster Tile Exchanging
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
I00
I01
I02
I03
I10
I11
I12
I13
I20
I21
I23
I22
I30
I33
I32
I31
W00
W11
W22
W33
W30
W20
W10
W01
W31
W21
W12
W02
W32
W23
W13
W03
HBM

## Slide 16
Inter-Cluster Tile Exchanging
Cluster00
Cluster01
Cluster02
Cluster03
Cluster10
Cluster11
Cluster12
Cluster13
Cluster20
Cluster21
Cluster22
Cluster23
Cluster30
Cluster31
Cluster32
Cluster33
I00
I01
I02
I03
I10
I11
I12
I13
I20
I21
I23
I22
I30
I33
I32
I31
W00
W11
W22
W33
W30
W20
W10
W01
W31
W21
W12
W02
W32
W23
W13
W03
HBM

## Slide 17
On-going work
Modeling FlooNoC in GVSoC
  FlooNoC: A Fast, Low-Overhead On-chip Network. RTL open-sourced: https://github.com/pulp-platform/FlooNoC
  Model in GVSoC + Calibrate timing with RTL simulation
  Modeling Mesh-NoC Connected Clusters
Enabling collective operations and extra computation operations in FlooNoC
  Multi-head Attention need: broadcasting
  When exploring Tensor Parallel, we need:
    In-network reduction
    In-network softmax, normalization …
Chi will be on holiday from 5th June to 17th June

## Slide 18: iDMA
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 19: iDMA GVSoC
Evaluating transposition extensions in Snitch
  End-to-end ML workloads
  Work still ongoing, results expected first meeting in June
Multichannel support
  Very important in NUMA memory systems
  RTL in Snitch completed
  GVSoC adaptations started

## Slide 20: Snitch Runtime -- Luca Colagrande is on Holiday till June 4th
Luca Colagrande colluca@iis.ee.ethz.ch