## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch
Viviane Potocnik vivianep@iis.ee.ethz.ch

## Slide 2
Current Progress
Just back from holiday
A scalable interconnect model is under developing in GVSoC
  Connect multiple clusters (redmule inside), host core, L2 memory, main memory (HBM)

## Slide 3
GEMM sizes in transformer
Most GEMMs in transformer models are big
  Smallest sizes are found in vision transformers 197 * 197 * 768
  Smallest sizes of GEMM to reach 97% uti on big Redmule (768MACs/Cycle)
    192 * 256 * 192

## Slide 4: SoftHier Progress Update
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 5
Current Progress
Working on expandable GVSoC iDMA model
  Simple implementation is working (Occamy can boot)
  No timing, just a memcpy-wrapper
  Model iDMA architecture ongoing, ETA 2-3 weeks
iDMA feature integration in Snitch is progressing
  Cleanup and maintenance operation
  In-system verification of basic operation
Started work on a new iDMA verification environment

## Slide 7
GVSoC RedMule Scaling-Out Experiment -- Recall
Scale-out RedMule CE array
  48 MACs/cycle RedMule(12x4) + 16 TCDM banks (16 element/cycle)
  192 MACs/cycle RedMule(24x8) + 16 TCDM banks (16 element/cycle)
  768 MACs/cycle RedMule(48x16) + 16 TCDM banks (16 element/cycle)
  768 MACs/cycle RedMule(48x16) + 32 TCDM banks (32 element/cycle)
Findings
  Larger RedMule
    Need much bigger input matrix to reach utilization close to 100%
    Need Bandwidth increase to avoid memory bound
    Unfriendly for small matrices
Chart: Matrix Dimension M-N-K
| 48-64-48 | 48-64-96 | 48-128-96 | 96-128-96 | 96-128-192 | 96-256-192 | 192-256-192
12x4-16BK-RT | 3132 | 6216 | 12360 | 24672 | 49296 | 98448 | 196848
24x8-16BK-RT | 1344 | 1920 | 3270 | 6348 | 12504 | 24792 | 49392
48x16-16BK-RT | 1536 | 2304 | 3072 | 5376 | 7680 | 12288 | 23808
48x16-32BK-RT | 768 | 1152 | 1536 | 2688 | 3840 | 6534 | 12684
12x4-16BK-Uti | 98.0843 | 98.8417 | 99.4175 | 99.6109 | 99.7079 | 99.8537 | 99.8781
24x8-16BK-Uti | 76.1905 | 80 | 93.945 | 96.7864 | 98.2726 | 99.1288 | 99.5141
48x16-16BK-Uti | 16.6667 | 22.2222 | 33.3333 | 38.0952 | 40 | 50 | 51.6129
48x16-32BK-Uti | 33.3333 | 44.4444 | 66.6667 | 76.1905 | 80 | 94.0312 | 96.878