## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch Luca Colagrande colluca@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 2
Cluster DMA (old model) performance Testing
Key DMA parameters
  Burst Length
  Num Outstanding Burst
Test settings
  Cluster (@1GHz) DMA transfer 1MB from DRAM to TCDM
    LPDDR4 @1.6GHz – Max 6.4GB/s
    DDR4-DIMM@993MHz – Max 15GB/s
    HBM channel @1GHz – Max 32GB/s
  Varying: Burst Length & Num Outstanding Burst
DMA saturate DRAM BW
  BL=512 Bytes
  #Outstanding = 256
PULP
Cluster
DMA
64B
Req: BL = 64B
64B
Resp:
64B
Latency
#Outstanding
CTRL
+
DRAM
Chart: DMA-HBM-ch
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
BL=64 | 7.09 | 9.42 | 11.26 | 11.72 | 12.69 | 13.12 | 13.82 | 15.22 | 18.02
BL=128 | 12.67 | 13.78 | 14.95 | 16.34 | 16.9 | 17.76 | 19.45 | 22.77 | 29.21
BL=256 | 19.68 | 21.57 | 23.15 | 24.24 | 25.31 | 27.45 | 31.46 | 39.18 | 51.45
BL=512 | 28.45 | 31.94 | 33.23 | 34.41 | 36.83 | 41.46 | 49.51 | 61.22 | 92.96
Chart: DMA-DDR4
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
BL=64 | 20.25 | 22.03 | 24.83 | 25.47 | 26.92 | 28.13 | 29.63 | 32.64 | 38.65
BL=128 | 29.12 | 30.1 | 31.43 | 33.64 | 35.65 | 37.31 | 40.56 | 46.96 | 58.5
BL=256 | 43.45 | 43.9 | 46.22 | 49.03 | 50.7 | 53.9 | 59.89 | 69.55 | 83.45
BL=512 | 54.93 | 57.87 | 60.68 | 62.33 | 65.41 | 69.71 | 76.65 | 86.45 | 90.07
Chart: DMA-LPDDR4
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
BL=64 | 26.5 | 44.89 | 55.76 | 58.22 | 61.33 | 63.82 | 67.3 | 74.27 | 79.66
BL=128 | 40.03 | 51.24 | 57.9 | 60.67 | 63.71 | 67.19 | 74.16 | 79.66 | 79.66
BL=256 | 54.21 | 57.79 | 59.95 | 63.87 | 67.29 | 74.11 | 79.66 | 79.66 | 79.66
BL=512 | 63.61 | 66.54 | 69.29 | 71.92 | 75.93 | 79.73 | 79.73 | 79.73 | 79.73

## Slide 3
Develop and test interconnect in GVSoC
built a scale-out system in GVSoC
  Test: every Cluster’s DMA is continue transferring data from HBM channel to Cluster TCDM
  We can model traffic with interconnect in GVSoC
Chart: Number of Cluster
| 1 | 2 | 4 | 8 | 16
Per-Cluster | 51.45 | 38.95 | 23.1825 | 11.66 | 5.8131
DRAM | 51.45 | 77.9 | 92.73 | 93.28 | 93.01
    DMA:BL = 256bytes, #Outstanding=256
Chart: Number of Cluster
| 1 | 2 | 4 | 8 | 16
Per-Cluster | 92.96 | 45.63 | 23.185 | 11.6575 | 5.82
DRAM | 92.96 | 91.26 | 92.74 | 93.26 | 93.12
    DMA:BL = 512bytes, #Outstanding=256

## Slide 4
Next step
On going:
  Modeling & Testing Multi-Cluster & Multi-HBM channel interconnected system

## Slide 5
iDMA Update
iDMA model is almost finished
  Timing accurate
  Arbitrary 1D transfers
  Model is expandable
  Will implement features beneficial in scaled-out systems
  Agile transfer launch and synchronization
iDMA is updated in Snitch, Update in Occamy pending
  Hardware is in, verification outstanding

## Slide 6: SoftHier Progress Update
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 7
Current Progress
A lot of maintenance and bug-fixing work in the last two weeks:
  PRs #99, #97, #32, #61, #100, #94, #83, #52, #62, #93, #92, #91, #87
Big efforts still ongoing:
  PRs #90, #102, #104
Efforts to port Snitch runtime to GVSoC will commence soon, as the Occamy model is developed