## Slide 1: QuantSparse 3D Biweekly 2025-03-25
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Hardware Architecture
  Choosing a compute unit
  Implementation status
Literature Review
  Low-Precision LLM Quantization
Discussion

## Slide 3: Hardware Architecture – Compute Unit
Two scales to consider
  Efficiency: performance and energy cost
  Flexibility: adaptability to ML workloads
Matrix engine
  Built for high-throughput dense matrix operations
   best energy efficiency for matrix-heavy workloads
  Non-matrix operations, e.g. row activation sparsity, are prone to underutilization
Scalar core
  For sequential processing and complex control flow  lower throughput and less energy efficient
  Best mapping flexibility

## Slide 4: Balancing Efficiency and Flexibility
Vector engine
  Computation speedup on vectorizable operations
   improved energy efficiency w.r.t scalar cores
  Compatible with vector-level operations and multi-granularity sparsity (structured and indexed)
+ Matrix ISA extensions
  Arm SME[6], Intel AMX[7], and IBM MMA[8]
  Direct handling of matrix operations  lowering the instruction fetch and setup overhead
  Minimizes the bandwidth demand between VRF and the VPUs  reduced energy consumption

## Slide 5: Workload Handling
Multi-granularity sparsity
  Structured sparsity (N:M, e.g. 2:4)  Vector engine, handled in VRF
  Unstructured sparsity in tile  RVV gathers on cluster L1 memory
  Unstructured sparsity in NoC  Packed gathers on HBM endpoints
Quantization
  Customized Microscaling format handled in the vector engine
  Small-group format with shared-scale minifloats and structured sparsity encoding (N:M)
  Two-stage sparsity (N:M structured + indexed gathers) bridges gap between low-precision elements and wide NoC / HBM

## Slide 6: Vector Engine Modeling – Where we are
Preliminary Spatz[9] model
  32-bit memory interface
  RV32 vector extension (RVV) support

## Slide 7: Vector Engine Modeling – What we need
Preliminary Spatz[9] model
  32-bit memory interface
  RV32 vector extension (RVV) support
Upgraded Spatz model
  64-bit memory interface
  ISA extension on sparsity handling
  ISA extension on Microscaling (MX) handling

## Slide 8: Vector Engine Modeling – What we need
Preliminary Spatz[9] model
  32-bit memory interface
  RV32 vector extension (RVV) support
Upgraded Spatz model
  64-bit memory interface
  ISA extension on sparsity handling
  ISA extension on Microscaling (MX) handling
Implementation status
  (In progress) Spatz GVSoC model 64-bit memory interface
  (In progress) A student project on RTL implementation of Spatz 2:4 sparsity handling with RVV ISA extension

## Slide 9: Literature Review: Low-Precision LLM Quantization
Quantization-aware training prohibitive
  Massive training effort (billions of weights)
  Focus on post-training quantization (PTQ)
Challenge: outliers in hidden activations
  Strong channel-wise spikes
  Naïve magnitude-based quantization strongly degrades past ~8-bit weights[2]
Prominent low-precision approaches:
  Quant. groups & outlier overlay (e.g. SpQR[1])
  Outlier compensation (e.g. SmoothQuant/+[2][3])
  Asymmetric shared scales (e.g. AMXFP4[4])
[5]

## Slide 10: Quantized Groups & Outlier Overlay: SpQR[1]
Identifies multiple magnitude patterns
  Row & column (token & channel)
  Attention heads & rotary embedding
  Unstructured outliers
Small weight groups with custom scales
  Quantize ≤32-weight groups to 3-4 bit
  Add two-level quantization statistics
<1% unstructured outlier overlay
  Full FP16 precision, stored in CSR (indexed)
Notably lower perplexity vs. 4-bit SoA

## Slide 11: Outlier Compensation: SmoothQuant/+[2][3]
Activation outliers stable per channel
  Direct correction is not performant
  Add per-channel smoothing s to weights, fuse inverse correction into prior layer
  Balance s between ideal weight and activation outlier compensation
SmoothQuant[2]: W8A8
  Uses efficient symmetric kernel  fast
  Minimal accuracy degradation vs. FP16
  Scales well to large models (175B)
SmoothQuant+[3]: scales to W4A16

## Slide 12: Asymmetric Shared Scales: AMXFP4[4]
MX accuracy degrades past ~FP6
  Rotation & small groups insufficient
  Issue: shared scales cannot encode nonzero group mean, only elements
Idea: Per-sign asymmetric scales
  One for +ve, one for –ve weights
  AMXFP4-FP8: asymm. FP8 scales  ~10% compute area overhead
Much closer to FP16 baseline than SoA methods at 4 bit
  Direct cast, no calibration!
  Still needs smaller groups (e.g. 32)

## Slide 13: References
[1] T. Dettmers et al., "SPQR: A sparse-quantized representation for near-lossless LLM weight compression." arXiv:2306.03078 (2023).
[2] G. Xiao et al., "SmoothQuant: Accurate and Efficient Post-Training Quantization for Large Language Models." arXiv:2211.10438 (2022).
[3] J. Pan et al., "SmoothQuant+: Accurate and Efficient 4-bit Post-Training Weight Quantization for LLM." arXiv:2312.03788 (2023).
[4] J. Lee et al., "AMXFP4: Taming Activation Outliers with Asymmetric Microscaling Floating-Point for 4-bit LLM Inference." arXiv:2411.09909 (2024).
[5] S. Liu et al., "LLM-FP4: 4-Bit Floating-Point Quantized Transformers.“ arXiv:2310.16836 (2023).
[6] F. Wilkinson, "An initial evaluation of arm’s scalable matrix extension." IEEE/ACM PMBS (2022).
[7] H. Kim et al., "Exploiting intel® advanced matrix extensions (amx) for large language model inference." IEEE CAL (2024).
[8] J. P. L. de Carvalho., "Compiling for the IBM matrix engine for enterprise workloads." IEEE Micro 42.5 (2022): 34-40.
[9] M. Perotti et al., "Spatz: Clustering Compact RISC-V-Based Vector Units to Maximize Computing Efficiency." arXiv:2309.10137 (2025).