## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch

## Slide 2
Benchmark LLama2 MLP block
Weight
Input
384
256
5120
Sequence length
384
256
13824
5120
Output
13824
Sequence length
384
384
iDMA
x6
iDMA
HBM Channel
x8
HBM Channel
    Max 384GB/s
    HBM2E: Max 410GB/s
iDMA
RedMule
Xbar
TCDM
#Banks = 32
Bank Width = 32b
Total Memory = 1MB
128GB/s
128GB/s
64GB/s
Problem Size
  Sequence length x 5120 x 13824
    Let the sequence length = 768
Implementation
  Clusters take care of different output tiles (384x384).
  At each round:
    iDMA transfers input matrix tile + weight matrix tile from HBM
    RedMule GEMM 384x256x384.
Variables
  RedMule Configuration:
    48x16 arrays -- 768 MACs/Cycle
    96x32 arrays -- 3072 MACs/Cycle
  Data format: FP8, FP16

## Slide 3
Results
Chart: RedMule-48x16-FP8
| redmule | idma
Busy | 3061119 | 855037
Idle | 0 | 2206082
Sync | 63375 | 63375
Chart: RedMule-48x16-FP16
| redmule | idma
Busy | 3131284 | 1418645
Idle | 0 | 1712639
Sync | 72370 | 72370
Chart: RedMule-96x32-FP8
| redmule | idma
Busy | 867815 | 737971
Idle | 0 | 129844
Sync | 24762 | 24762
Chart: RedMule-96x32-FP16
| redmule | idma
Busy | 938220 | 1418645
Idle | 480425 | 0
Sync | 64407 | 64407
Chart: Utilization
| RedMule-48x16-FP8 | RedMule-48x16-FP16 | RedMule-96x32-FP8 | RedMule-96x32-FP16
RedMule Compute Uti | 0.94387 | 0.92055 | 0.82601 | 0.49714
HBM BW Uti | 0.221 | 0.43109 | 0.77363 | 0.93122
End-to-End System Performance
  Occamy + 48x16 RedMule, 410 GB/s HBM
    FP8: 34.6 TOP/s
    FP16: 34.3 TOP/s
  Occamy + 96x32 RedMule, 410 GB/s HBM
    FP8: 120.9 TOP/s
    FP16: 72.3 TOP/s
Memory-Bound When:
  RedMule 96x32
  FP16 GEMM
Improvement:
  Inter-Cluster Data Reuses
  Horizontal DataMove

## Slide 4
Leverage Inter-Cluster Data Reuses
Modeling
  Previous model only contain Cluster-to-HBM Interconnect
  Modeling Cluster-to-Cluster Interconnect
    Also triggered by iDMA in each Cluster
    Modeling Finished
Current Progress:
  New Code for LLama2 MLP Layer
  Take Inter-Cluster Transfer into account

## Slide 5: iDMA RTL
Busy working on the tapeout (Mid-May)

## Slide 6: SoftHier Progress Update
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 7: Snitch Runtime
Mostly busy on “transformers on Occamy” paper
Now occupied on another paper till mid-May
As part of these paper efforts…
Work on some PRs to improve the runtime
  Fix various compiler warnings #134
  extern declarations to distribute as static library #133
Fix a long-reported bug in printf function #13