## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch

## Slide 2
Overall Update
We Modeled NoC-Based Scalable System in GVSoC
We Calibrated NoC Model’s Timing
We Benchmarked Cluster Synchronization Scheme

## Slide 3
FlexCluster: Parameterizable NoC-Based Scalable System
R
R
DATA NoC Router
SYNC NoC Router
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
HBM ch
Core 0
Core 0
…
Core n
RedMule
iDMA
Infinite Instruction Mem
TCDM
CTRL
REG
Interconnect
To DATA NoC Router
To SYNC NoC Router
Cluster
Features
  Two separate NoC bus
    DATA NoC: wide link, transfer bulk data
    SYNC NoC: narrow link, cluster synchronization
  Infinite Instruction memory
    Ignore I$ fetch overhead
Fully Parameterizable
  Configure file and push button
      #Cores, RedMule config
      L1 (TCDM) size & BW
      #Clusters (#row, #col)
      #HBM channels and placement
      NoC link BW
SW stack ready

## Slide 4
Calibrate NoC Model’s Timing
DATA NoC Setting
  Link BW = 512b/cycle
  XY routing algorithm
  Each cluster inject DMA transfer 1MB data
Patterns
  Scatter O(n2)
  Dialog O(n)
  Round Shift O(1)
    Deviation due to sync
Scatter
Dialog
Round Shift
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 32768 | 73728 | 131072 | 204800 | 294912 | 401408 | 524288 | 663552 | 819200 | 991232 | 1179648 | 1384448 | 1605632 | 1843200 | 2097152 | 2367488 | 2654208 | 2957312 | 3276800 | 3612672 | 3964928 | 4333568 | 4718592 | 5120000 | 5537792 | 5971968 | 6422528 | 6889472 | 7372800 | 7872512 | 8388608
NoC Model | 8822 | 16502 | 49260 | 98509 | 163958 | 245950 | 344256 | 458957 | 589942 | 737470 | 901210 | 1081534 | 1278142 | 1491034 | 1720438 | 1966286 | 2228342 | 2506942 | 2801854 | 3113150 | 3440831 | 3784794 | 4145242 | 4522174 | 4915390 | 5324990 | 5750974 | 6193242 | 6651994 | 7127230 | 7618752 | 8126669
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 8192 | 8192 | 16384 | 16384 | 24576 | 24576 | 32768 | 32768 | 40960 | 40960 | 49152 | 49152 | 57344 | 57344 | 65536 | 65536 | 73728 | 73728 | 81920 | 81920 | 90112 | 90112 | 98304 | 98304 | 106496 | 106496 | 114688 | 114688 | 122880 | 122880 | 131072
NoC Model | 8834 | 8733 | 8859 | 16600 | 16501 | 24805 | 24790 | 32988 | 32889 | 41185 | 41193 | 49387 | 49377 | 57599 | 57471 | 65770 | 65670 | 73969 | 73975 | 82157 | 82089 | 90357 | 90358 | 98543 | 98543 | 106739 | 106747 | 114943 | 114943 | 123123 | 123127 | 133127
Chart: Mesh NoC Dimension
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Thereotical | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192 | 8192
NoC Model | 8834 | 8734 | 8858 | 8848 | 8825 | 8932 | 8849 | 8879 | 8903 | 9044 | 8993 | 9132 | 9182 | 9138 | 9185 | 9226 | 9311 | 9492 | 9551 | 9644 | 9627 | 9703 | 9797 | 9980 | 10078 | 10180 | 10279 | 10299 | 10415 | 10628 | 10645 | 10746

## Slide 5
Cluster Synchronization Scheme
C
C
C
C
C
C
C
C
C
Sync All
C
C
C
C
C
C
C
C
C
Sync XY
Chart: Synchronization Overhead
| 1 | 2 | 4 | 8 | 16 | 32
Sync_ALL | 88 | 98 | 118 | 119 | 288 | 1072
Sync_XY | 113 | 171 | 169 | 169 | 192 | 248
Time
Global Sync1
Global Sync2
Synchronization overhead can not be ignored
  Normal synchronization need every cluster to access the same mutex
  O(n2)
New scalable synchronization scheme
  First sync row-wise clusters parallelly
  Then sync the latest cluster of each row
  O(n)

## Slide 6
Next Step
Design Space Exploration on FlexCluster
  RedMule CE array, TCDM size, #Clusters …
Writing GEMM kernels in common LLM (with various sequence length and batch size)
  Multi-head attention
  MLP
Kernels need to automatedly adapt to different FlexCluster configuration

## Slide 7
Other Progress update
Luca C. did maintenance work on the snitch cluster and runtime
  Merged PRs #137, #149, #151, #153, #156, #157
  Closed issues #98, #139
Thomas attended the RSIC-V summit, is currently busy with chip testing for ISSCC paper