## Slide 1: SoftHier Progress Update
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 2
Current Status
Modeling Redmule + Occamy System in GVSoC
  Snitch cluster (iDMA equipped) – done
  Extending Snitch cluster with RedMule – done
  Quadrant modeling – done
  Top-level modeling:
    Host Core CVA6 & Periphrals – done
    HBM & Interconnect – done
    SPM & C2C-link– on going
  RedMule in Occamy Functional testing – done
    Runtime is aligned with previous experiment on Pulp-Cluster
  iDMA testing – done, showing results in this meeting

## Slide 3
iDMA Bandwidth Testing -- Setup
HW Configuration
  AXI Bus [Cluster, Quadrants, HBM.ch]
    Width =512b, Max.BW=64GB/s
  6 Quadrants, 4 Clusters per Quadrant
    6 Quadrants Max.BW = 384GB/s
  8 HBM.ch, 4K address space interleaved
    HBM2 total Max.BW = 256GB/s
    HBM2E total Max.BW = 410GB/s
iDMA test program
  Each cluster transfer 256KiB data from HBM to TCDM
  Global barriered before & after iDMA transfer
  Enable Clusters in quadrant-interleaving fashion
iDMA
x6
iDMA
HBM Channel
x8
HBM Channel
#Cluster=1
#Cluster=2
#Cluster=6
#Cluster=7
    Max 384GB/s
    HBM2: Max 256GB/s
    HBM2E: Max 410GB/s

## Slide 4
iDMA Bandwidth Testing -- Results
Best HBM BW utilization reached
  94% BW uti – HBM2
  91% BW uti – HBM2E
When #Cluster = 1
  iDMA BW= 53GB/s, 57GB/s
  Almost saturate Cluster AXI port Max.BW(64GB/s)
When each Quadrant enable 1 Cluster
  HBM2 – 214 GB/s – 83% HBM Uti
  HBM2E- 257 GB/s – 62% HBM Uti
Why HBM2E curve is jagged?
  Imbalanced workload among Quadrants
Chart: #Enabled Snitch Cluster
HBM2-256GB/s | 53.3789 | 83.5652 | 118.1184 | 161.3442 | 185.707 | 214.0242 | 215.6803 | 223.4341 | 228.8579 | 233.3695 | 234.1902 | 233.3972 | 236.3951 | 237.4493 | 236.0098 | 237.1673 | 237.4999 | 238.4572 | 236.9072 | 237.2451 | 238.1169 | 236.9809 | 238.1809
HBM2E-410GB/s | 57.7283 | 83.4588 | 135.1026 | 173.4904 | 217.4386 | 257.8888 | 221.4321 | 264.3247 | 290.3034 | 316.7903 | 350.2045 | 354.728 | 299.1198 | 312.7677 | 325.6987 | 345.922 | 363.1691 | 377.4874 | 329.9812 | 337.5317 | 362.125 | 371.0699 | 373.9572
    HBM2: Max 256GB/s
    HBM2E: Max 410GB/s
91% HBM2E Uti
94% HBM2 Uti
Chart: 
| Q0_C0 | Q1_C0 | Q2_C0 | Q3_C0 | Q4_C0 | Q5_C0
IDEL | 831 | 262 | 369 | 612 | 0 | 122
iDMA | 5268 | 5624 | 5588 | 5416 | 5744 | 5693
IDEL | 0 | 213 | 142 | 71 | 355 | 284
Chart: 
| Q0_C1 | Q0_C0 | Q1_C0 | Q2_C0 | Q3_C0 | Q4_C0 | Q5_C0
IDEL | 91 | 743 | 414 | 616 | 280 | 283 | 0
iDMA | 6479 | 7544 | 5106 | 5070 | 5026 | 5166 | 5164
IDEL | 1717 | 0 | 2767 | 2601 | 2981 | 2838 | 3123

## Slide 5
Next Plan
Model L2 Memory (SPM)
Benchmark iDMA + RedMule running LLM’s GEMM

## Slide 6
iDMA updates
2 publications completed followed by a week of holidays
Tapeout ongoing (mid May)
iDMA
  Newest version integrated in Occamy RTL and GVSoC model
  In progress: evaluating transposition engine in Occamy
  Verilator testbench soon ready

## Slide 7: SoftHier Progress Update
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 8
Snitch runtime updates
Busy full time on a paper: “Transformers on Snitch/Occamy”
Useful for SoftHier:
  Insights on latency breakdown of transformers in Occamy and relevant matrix sizes
  Snitch runtime developments:
    Added bounds check on dynamic L1 heap allocations
Review Germain’s PR #126
  Creates a GVSoC-specific Snitch runtime
  Required to have a dedicated putchar implementation for OpenOCD semi-hosting