## Slide 1: QuantSparse 3D Biweekly 2025-05-20
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Agenda
Progress Update
  2.5D/3D packaging SoA
  Beyond SoA: 3D and 3.5D opportunities
Timeline
Discussion

## Slide 3: 2.5D Packaging
Multiple active semiconductor dies are placed side-by-side on an interposer
  Enables the integration of diverse components into a single package
  Reduced interconnect length  lower latency, improved power efficiency
  Package size reduction
Flip Chip
Flip Chip w/ <100μm pitches
Extremely common
Landing pads on PCB, substrate, or other wafer
Chip placed on top with bump contacts
Involvement is limited to a small number of firms
A flood of different packaging types

## Slide 4: 2.5D Packaging
Standard
Flip Chip
TSMC InFO-R
Organic laminate clad with copper
Wires are built around the core, both sides  many layers, redistributing signal and power
Silicon as substrate
High I/O density
Complex routing
Multiple chips
InFO-SoIS
Apple Sillcon
14 RDL  complex interconnect
InFO-SoW
Fanout size as an entire wafer
Tesla Dojo D1
InFO-L
Passive silicon interconnect between multiple dies
CoWoS-R
CoWoS-S
CoWoS-L
Intel EMIB
Silicon bridge inside of organic substrate
Kaby Lake G, FPGAs
NVIDIA GPUs
ASE FoCoS
Samsung FOSiP

## Slide 5: 3D Packaging
Stacking multiple active semiconductor dies on top of each other
  Further reduces interconnect lengths  minimizing signal delays and power consumption
Micro Bump
Hybrid Bonding
Enable denser integration
Lower parasitics (resistance, capacitance)
More complex and higher cost
Ponte Vecchio GPU (36um)

## Slide 6: 3D Packaging – Hybrid Bonding
TSMC SoIC
L3 cache vertically integrated, sits in the middle of compute chiplet
3x cache size, 4 cycles latency
19% perf. Improvement on average
AMD Zen 3 (9um)
Vertically integrated power-management die
40% faster, 16% less energy consumption
Graphcore BOW
Foveros Direct
Samsung Xcache
Meta 3D-Mem
YMTC Xtacking

## Slide 7: Beyond SoA: 3D and 3.5D Opportunities
F2B (repeatable) hybrid bonding
  TSMC SoIC-X: 25µm pitch in 2025[1]
  Enables 3D stacks (cubes) of logic and/or SRAM (e.g. 3D V-cache[2])
  Can be combined with interposer and HBM stacks
Consider this in 3D explorations
  Model multi-layer logic (3D mesh): z-direction links as hybrid bonds
  Explore logic-SRAM stacks (L1/L2?)
  Consider logic-DRAM (HBM) stacks?
F
B
F
B
F
B
F
B
Interposer
HBM
HBM
HBM
HBM
HBM
HBM
HBM
HBM

## Slide 8: References
[1] A. Shilov, “TSMC's 3D Stacked SoIC Packaging Making Quick Progress, Eyeing Ultra-Dense 3μm Pitch In 2027,” 2024
[2] A. Smith et al., "11.1 AMD InstinctTM MI300 Series Modular Chiplet Package – HPC and AI Accelerator for Exa-Class Systems," ISSCC, 2024