## Slide 1: QuantSparse 3D Biweekly 2025-06-03
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Previous Progress
  Literature Review
  SoA LLM sparsity, quantization format, and 2.5D/3D advanced packaging tech.
  Proposed vector-engine-based multi-cluster architecture
  Proposed GVSoC router extension for 3D integration
  WP1
  Ongoing RTL and GVSoC modeling of HBM endpoint packing scheme
  Ongoing RTL and GVSoC modeling of Spatz N:M sparsity handling
  Ongoing RTL and GVSoC modeling of Spatz MX format handling
  WP2
  Memory allocation runtime for model-to-hardware mapping
  Ongoing model-to-hardware mapping software environment

## Slide 3: Agenda
Progress Update
  Spatz N:M sparsity format
    Gather operation at VLSU
    Gather operation in VRF
  Spatz MX format
    Baseline kernel implementation and insights
Timeline
Discussion

## Slide 4: Spatz N:M sparsity: VLSU
Effective elements gathered from L1 to VRF through VLSU
  No VRF overhead for ineffective elements storage
  Data reuse is impossible across weight rows
Baseline implementation  leverage on RVV indexed load instruction (vluxeiX.v)
  Minimum 8-bit indices encoded in the instruction semantics, used in VLSU for address generation  VRF waste
  Index tensor used in N:M format has different semantics  Index preprocessing is required
Progress
  vluxeiX.v instructions implemented in GVSoC with timing model (PR #124)
  RTL implementation ongoing

## Slide 5: Spatz N:M sparsity: VLSU
Baseline benchmark
  Cycles for input load do not scale with element bit-width
  Reason: vluxeiX.v does not assume any data storage patterns  loading low precision elements cannot benefit from wide bus-width
Our proposal: customized indexed load instructions
  Address generation in VLSU uses N:M index tensor directly
  Gather all effective elements per bank read, leveraging on N:M format index patterns

## Slide 6: Spatz N:M sparsity: VRF
Effective elements gathered inside VRF with vrgather.v-like instruction
  Data reuse is possible across weight rows
Baseline implementation: customized for N:M format, currently with 64-bit element and 2-bit index
  Could be extended to support lower precision elements and more N:M formats
Progress
  RTL implementation finished and passed function verification
  Ongoing SpMV kernel development and benchmark

## Slide 7: Spatz N:M sparsity: VRF
Efficient gather handling is the key
  Underutilized VRF-to-VFU bandwidth for ineffective element bubbles
  Mixed vector length after gather operations  introduces configuration overhead

## Slide 8: Spatz N:M sparsity: VRF
Efficient gather handling is the key
  Underutilized VRF-to-VFU bandwidth for ineffective element bubbles
  Mixed vector length after gather operations  introduces configuration overhead
Potential remedy
  vrgather.v utilizes 2 read ports and 1 write port  reuse the third VRF read port, while requires VRF redesign
  Mixed vector length instruction set extension[1] through arbitrary register groupings and hardware strip-mining

## Slide 9: Spatz MX Format
Inner product
  Producing one full dot product for each output element per inner loop  requires reduction before each scaling and accumulation
  Reduction is slow in Spatz: 75% runtime in reduction
Outer product
  Elements from different blocks are produced in parallel
  Requires both matrices to be stored in row-major layout (or strided load is required)  may not be applicable (i.e. attention)

## Slide 10: Spatz MX Format
...
for i in BLOCK:
// load
scalar load a_i, ...
vector load b, ...
// widen
fcvt.h.b a_i
vfwadd.vf b, ...
// comp
vfwmacc.vf c, b, a_i
// load scale
vle.v vd1, ...
ld s1, ..
// apply scale
...
Outer product
  Elements from different blocks are produced in parallel
  Requires both matrices to be stored in row-major layout (or strided load is required)  may not be applicable (i.e. attention)
  mxfp8_matmul_fp32_outer_lmul4_2x (64 × 64 × 64)

## Slide 11: Spatz MX Format
...
for i in BLOCK:
// load
scalar load a_i, ...
vector load b, ...
// widen
fcvt.h.b a_i
vfwadd.vf b, ...
// comp
vfwmacc.vf c, b, a_i
// load scale
vle.v vd1, ...
ld s1, ..
// apply scale
...
Overhead analysis
  ~50% cycles for casting format and applying scale
  mxfp8_matmul_fp32_outer_lmul4_2x (64 × 64 × 64)

## Slide 12: Progress Update
  WP1
  Spatz vector load instruction modeling in GVSoC + baseline impl. performance analysis
  Spatz VRF gather operation RTL implementation and impl. analysis
  Spatz MX format baseline kernel implementation + overhead breakdown

## Slide 13: References
[1] L. Jiang, “Unlimited Vector Processing for Wireless Baseband Based on RISC-V Extension” 2025, Arxiv Preprint: https://arxiv.org/abs/2504.10832