## Slide 1: QuantSparse 3D Biweekly 2025-06-17
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  Spatz vector load instruction modeling in GVSoC + baseline impl. performance analysis
  Spatz VRF gather operation RTL implementation and impl. analysis
  Spatz MX format baseline kernel implementation + overhead breakdown

## Slide 3: Agenda
Progress Update
  Spatz N:M sparsity format
    Gustavson’s algorithm for activation sparsity handling
    Spatz GVSoC model supports FP8 format + Baseline MatMul implementation
  Spatz MX format
    Proposed MX-dotp ISA extension
Timeline
Discussion

## Slide 4: Spatz Activation Sparsity
Gustavson’s algorithm
  Scalar-vector multiplication between a single element from the activation tensor and a weight vector, producing a vector of the output tensor
  No vector reduction needed

## Slide 5: Spatz Activation Sparsity
Gustavson’s algorithm
  Scalar-vector multiplication between a single element from the activation tensor and a weight vector, producing a vector of the output tensor
  No vector reduction needed
Compatible with weight tensor’s N:M format
  The weight tensor is stored in the compact N:M format with the index tensor
  Effective elements in the output vector need to be gathered, accumulated, and scattered depending on weight indices

## Slide 6: Spatz Activation Sparsity
Gustavson’s algorithm
  Scalar-vector multiplication between a single element from the activation tensor and a weight vector, producing a vector of the output tensor
  No vector reduction needed
Compatible with weight tensor’s N:M format
  The weight tensor is stored in the compact N:M format with the index tensor
  Effective elements in the output vector need to be gathered, accumulated, and scattered depending on weight indices
Activation sparsity is natural supported
  Skip the entire scalar-vector multiplication
  Activation elements become conditions to trigger computation
  Compatible with GEMV

## Slide 7: Spatz GVSoC Model
Extended with FP8 (E5M2) datapath
  Added FP8 unit instruction tests
  Implemented FP8 Gustav Matmul baseline kernel (FP8 accumulation, non-sparsity, non-quantization)
  Next-step: consider activation and weight sparsity, with performance analysis
https://github.com/gvsoc/gvsoc/tree/soft_hier_release(#129)

## Slide 8: Spatz MX Format
Matmul performance analysis
  The inner-product approach is discarded to avoid expensive vector reduction
  Benchmarked outer-product approach compared with non-MX baseline (computation scale: 64xNx64)
    Low performance of MX8 software kernels
    50% of runtime is for ‘useful’ MAC operations
    30% for the RVV programming model for mixed precision operations
    16% for combining two E8M0 scales, and merging with the accumulated dot product element
  Native hardware support via custom ISA extensions  fully utilizes VPU throughput and exploits MX format efficiency

## Slide 9: Spatz MX Format
Vmxdotp extension
  Computes an MX dot product of block size k and adds it to an FP32 accumulator
  Main difficulty: The operation requires 5 different operands, while existing RVV instructions operate on at most three source operands
  For proof-of-concept experiment, and keep compatibility with N:M format handling in Gustav, we first focus on a special case:
    Accumulator, one element vector, one scale are read from the VRF
    The other element vector and scale provided by two scalar registers
  Vector-scalar instruction variance
    32-bit encodings utilizing reserved opcodes, recommended for experimental extensions

## Slide 10: Progress Update
  WP1
  Gustavson’s algorithm-based activation and weight sparsity handling
  Spatz GVSoC model with FP8 datapath, instruction tests, and Gustav MatMul baseline implementation
  Spatz MX format ISA extension initial discussion