## Slide 1: QuantSparse 3D Biweekly 2025-08-19
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Progress Recap
  WP1
  SpMM kernel implementation, optimization, and benchmark with vfwx_.vf instructions

## Slide 3: Agenda
Progress Update
  Spatz N:M sparsity format
    Extending vfwx_.vf instruction with multi-format support
    Performance benchmark, roofline model analysis
    N:M format wrap-up
Timeline
Discussion

## Slide 4: Recap: SpMM kernel imple. with vfwx_.vf instructions
Unroll
Preload
Activation elements are passed through FP registers
  Unrolled 4x to increase the data reuse of the weight vectors
Weight elements are loaded as vectors
Preload 2x to remove the WAR dependency
Control overheads:
  Address incremental calculation for loading elements
  Explicit scalar load instructions for activation
Scatter / Gather

## Slide 5: Recap: Speed Up Results
Results:
  Up to 1.60x speedup with long vl
  Lower performance with shorter vl, as a result of higher control overhead (address calculation)  Post-Incrementing vector Load & Store Instructions

## Slide 6: Roofline Analysis
System configurations
  1x Spatz4 per SoftHier Cluster
  4x 64-bit PEs per Spatz4
   Peak performance 32 MACs/cycle (FP8)
  4x 64-bit LSUs per Spatz4
   L1-to-PE bandwidth 32B/cycle

## Slide 7: Roofline Analysis: Impact of Efficient VReg Gather OPs
No special handling for output accumulations
Benchmarked with 32x32x1024 SpMM

## Slide 8: Roofline Analysis: Impact of Efficient VReg Gather OPs
No special handling for output accumulations
  For a 50% sparsity rate (e.g. 1:2), only half of the output accumulations are effective
   Effective VPU throughput is halved
Effective
Effective

## Slide 9: Roofline Analysis: Impact of Efficient VReg Gather OPs
No special handling for output accumulations
  For a 50% sparsity rate (e.g. 1:2), only half of the output accumulations are effective
   Effective VPU throughput is halved
  Worsened for a higher sparsity rate
  Performance is constrained by the effective VPU throughput
32 MACs/cycle
16 MACs/cycle
8 MACs/cycle
4 MACs/cycle
2 MACs/cycle
1:2
1:4
1:8
1:16
Benchmarked with 32x32x1024 SpMM

## Slide 10: Roofline Analysis: Impact of Efficient VReg Gather OPs
Gathering effective output accumulations
  With VSLIDE unit, within VRegs, adding buffers. Or combined.
  For a higher sparsity rate, multiple combined methods are required  larger hardware overhead should be expected
Gather

## Slide 11: Roofline Analysis: Impact of Efficient VReg Gather OPs
32 MACs/cycle
16 MACs/cycle
8 MACs/cycle
4 MACs/cycle
2 MACs/cycle
1:2
1:4
1:8
1:16
Gathering effective output accumulations
  With VSLIDE unit, within VRegs, adding buffers. Or combined.
  For a higher sparsity rate, larger hardware overhead should be expected
Performance improvement is promising
  Highly depends on the gathering strategies and hardware implementation
6.1x
1.9x
Benchmarked with 32x32x1024 SpMM

## Slide 12: Roofline Analysis: Impact of Control Instructions
32 MACs/cycle
16 MACs/cycle
8 MACs/cycle
4 MACs/cycle
2 MACs/cycle
Benchmarked with 32x32x1024 SpMM
Performance is still detached from the roofline
  Impacts from: Control instructions for address calculation and, explicit scalar activation elements loading

## Slide 13: Roofline Analysis: Impact of Control Instructions
Performance is still detached from the roofline
  Impacts from: Control instructions for address calculation and, explicit scalar activation elements loading
  More prominent with a higher sparsity rate. For the vfwxmacc.vf instruction: 16 cycles for 1:2 format 2 cycles for 1:16 format @ Spatz4 FP8 inputs

## Slide 14: Roofline Analysis: Impact of Control Instructions
Scalar activation streaming
Address post increment

## Slide 15: Roofline Analysis: Impact of Control Instructions
32 MACs/cycle
16 MACs/cycle
8 MACs/cycle
Benchmarked with 32x32x1024 SpMM
Removing the control instructions pushes the performance to the roofline
  Additional hardware overhead required

## Slide 16: Roofline Analysis: Impact of Higher Sparsity Rate
32 MACs/cycle
16 MACs/cycle
8 MACs/cycle
Benchmarked with 32x32x1024 SpMM
Lower AI
  1:2  1:4: doubled sparsity rate (2xSR):  Halved #MACs, less impact on #Bytes
Lower performance
  More prominent control overheads

## Slide 17: Roofline Analysis: Impact of Sparsity formats
32 MACs/cycle
Benchmarked with 32x32x1024 SpMM
Lower AI
  More bits required to index 4:8 format than 1:2 format  higher
Same performance
  Sparsity formats with the same rate have negligible impact on performance
1:2
4:8

## Slide 18: Roofline Analysis: Impact of Comp. Dimensions (M)
Same AI
  M scales #Bytes and #MACs with the same ratio
Same performance
  M only determines the number of middle loops

## Slide 19: Roofline Analysis: Impact of Comp. Dimensions (N↑)
32 MACs/cycle
Benchmarked with M=32, 1:2 format
Higher AI
  N scales #MACs with a higher ratio compared to #Bytes
Same performance
  N only determines the number of inner loops
N=128
N=32

## Slide 20: Roofline Analysis: Impact of Comp. Dimensions (N↑)
32 MACs/cycle
Higher AI
  N scales #MACs with a higher ratio compared to #Bytes
Same performance
  N only determines the number of inner loops
1:2
1:4
1:8
1:16
Benchmarked with M=32, P=1024

## Slide 21: Roofline Analysis: Impact of Comp. Dimensions (P↑)
32 MACs/cycle
Higher AI
  P scales #MACs with a higher ratio compared to #Bytes
Higher performance
  More tolerant to the control overhead
  Confined by VLEN and VReg grouping
1:2
1:4
1:8
1:16
Benchmarked with M=N=32

## Slide 22: Conclusion: Structure Sparsity Handling
Effective gathering operation for output accumulation is essential
  Combined strategies from the VSLIDE unit, VReg, and buffers
  Higher hardware overhead for formats with higher sparsity rates
Removing control instruction overhead improves the performance
  With activation streaming and address post increment
  Additional hardware overhead
Higher sparsity rate  Lower AI
  Moving towards the memory-bound region
Workload tiling strategy
  Tiling on the M dimension has a negligible impact on performance, weight duplication across clusters
  Tiling on the N dimension requires inter-cluster reduction
  Keep the P dimension as large as possible  Higher performance

## Slide 23: Progress Update
  WP1
  Structure sparsity format handling wrap-up