## Slide 1: QuantSparse 3D Kickoff
Integrated Systems Laboratory (ETH Zürich)
Bowen Wang bowwang@iis.ee.ethz.ch Paul Scheffler paulsc@iis.ee.ethz.ch
Luca Benini lbenini@iis.ee.ethz.ch

## Slide 2: Team Introduction
Paul Scheffler
  BSc & MSc at ETH Zurich
  Research Experience
    Sparse Workload HW Acceleration
    Energy-efficient RISC-V Systems
    Manycores and Interconnects
    SoC Design
Bowen Wang
  BSc at Harbin Institute of Technology
  MSc at ETH Zurich
  Research Experience
    Manycores
    Network-on-Chip
    DNN Compiler

## Slide 3: Background
Context and Motivation
  Transformers in LLM  Foundation Model paradigm
  Energy scaling has lagged behind performance scaling
  Sparsity and Quantization – reducing computation, memory footprint, and bandwidth
  Computation distribution across memory hierarchy w.r.t. computation intensity
  Network mapping, deployment, and fast simulation
  Exploit three-dimensional heterogeneous integration technology – from 2.5D-Chiplet to 3D-stacked IC
QuantSparse3D: Aims and Objectives
  Mitigate energy bottlenecks by improving performance under power constraints

## Slide 4: Project Structure
WP1: Architectural exploration, definition, and sizing at chiplet level
  Simulation models of key building blocks
    Compute engine, memory hierarchy, on-chip interconnect, and memory endpoint
  RTL models of key building blocks for power, performance, and area estimation
    Access PPA using post-backend estimations
WP2: System-level modeling and design
  Configuration space Exploration
    Dimensioning single chiplet, 3D-stacked memories, and scaling to multiple chiplets
  Flexible model-to-hardware mapping using standardized high-level specifications
WP3: Integration, benchmarking, and performance tuning
  Access performance, energy efficiency, and scalability
  Extend models to the emerging technologies
    NV memories, 3D-DRAM, and HBM4 with the upcoming 3D stacking options

## Slide 5: Milestones
2025-02
2025-04
Literature Review
2026-02
2026-06
2027-02
  WP1 & WP2
  Chiplet architecture refinement
  Tuning of performance and power models
  Software extension to enable end-to-end inference
WP1, WP2
Start
Year 1
WP3 Start
Year 2
  WP1
  Architectural modeling and design of the chiplet architecture
  Build and synthesize parameterized RTL models to assess PPA
  WP2
  System modeling of multi-chiplet fabrics and 3D-stacked memories
  Software environment for model-to-hardware mapping with open-sourced environments and specifications
  Design space exploration of system configurations using simplified end-to-end models and microkernels
  WP3
  Performance analysis and efficiency assessment on end-to-end workload
  Explore configuration space for a significant mix of workload at different sparsity level and leveraging aggressive quantization

## Slide 6: Deliverables
2025-02
2025-04
Literature Review
2026-02
2026-06
2027-02
WP1, WP2
Start
Year 1
WP3 Start
Year 2
  Report and open-source release on:
  Architectural specification, preliminary design, and PPA efficiency assessment
  System-level specification, simulation model, and software
  Report and open-source release on:
  System model and integrated HW-SW simulation
  Benchmark exploration, architectural assessment, and roadmap

## Slide 7: State of the Art: GPUs
So far: 2:4 structured sparsity [1] only
  Introduced with Nvidia Ampere (2020)
  2 values in every 4-block must be zero
  Up to 2× smaller & faster than dense
Gradual adoption of low-precision formats
  Lower FP precisions every generation
  Driven by ML/AI applications
GB100: <8b microscaling (MX) [2] formats
  Blocks of values with shared scale factor
  INT and FP formats, varying block sizes
Year | GPU | Low-precision (<32b) Formats | Sparsity
2020 | A100 | FP16, BF16, INT8 | 2:4 structured
2023 | H100 | FP8, FP16, BF16, INT8 | 2:4 structured
2023 | MI300X | FP8, FP16, BF16, INT8, INT16 | 2:4 structured
2025 | GB100 | FP8, FP16, BF16, INT8, MXFP4, MXFP6, MXFP8, MXINT8 | 2:4 structured
[2] B. D. Rouhani et al., “OCP Microscaling Formats (MX) Specification,” OCP
[1] Nvidia, “Nvidia A100 Tensor Core GPU Architecture,” Nvidia
[1]

## Slide 8: State of the Art: Commercial AI Accelerators
Common architectural features
  Parallel processing and efficient data movement
  Clusters of tensor/vector units
  Connected via a 2D NoC mesh
Streaming dataflow model for handling unstructured sparsity
Year | Design | Architectural Highlight | Data Format | Sparsity
2022 | Groq GroqChip | Functional-sliced microarchitecture | FP/INT32, FP/INT16, INT8 | Unstructured
2023 | Microsoft Maia 100 | Tiles of TU, hierarchical 2D NoC mesh | FP32, BF16, MXFP9, MXFP6 | N.A.
2023 | Tenstorrent Blackhole | Cluster of TU, 2D NoC mesh | FP/INT/TF32, INT/BF16, FP8, INT8, Block FP2/4/8 | Unstructured
2024 | SambaNova SN40L | Configurable PE, 2D NoC mesh, Streaming dataflow | FP/INT32, BF16, INT8 | Unstructured
2024 | Furiosa RNGD | Cluster of tensor contraction units, 2D NoC mesh | BF16, INT8, FP8, INT4 | N.A.
2024 | Huawei Ascent 910C | Cluster of cube and vector units, On-chip mesh | FP/INT32, FP16, INT8 | N.A.
2024 | d-Matrix Corsair | CIM , Vector engine, Hierarchical interconnect | MXINT16, MXINT8, MXINT4 | N.A.
2024 | Cerebras WSE-3 | Cluster of TU, 2D NoC mesh, Streaming dataflow | FP/BF16, INT8 | Unstructured
Quantization trend
  8-bit quantization dominates AI accelerators
  Emerging sub-8-bit and block quantization

## Slide 9: State of the Art: Sparse Accelerators in Research
Target different abstraction levels
  Direct ML workload acceleration
  Sparse linear/tensor algebra
  General-purpose stream operations
Usually target low (ML) precisions
Almost always unstructured
  Bitmap or indexed sparse encoding depending on required sparsity range
Trend toward higher flexibility
  Less structure, higher range, flexible dataflow, single- and dual-side sparsity
Year | Design | Silicon | Architecture | Function | Sparsity Handling Mechanisms | Data Flow | Data Formats | Sided- ness | Sparse encod. | Sparse range
2019 | Dadu et al.[1] | ✗ | CGRA | General-purpose str. ops | Indirection, Inters., Union | Flexible | FP32, FP64 | Both | Indexed | High
2020 | SIGMA[2] | ✗ | MAC PE Array | Sparse-Sparse Matmul | Distribution Networks | Fixed | BF16 | Dual | Bitmap | Med.
2022 | Huang et al. [3] | ✓ | Multi-Accelerator | Sp. CNN & GCN infer. | Distribution Networks | Fixed | INT8 | Single | Bitmap | Med.
2023 | Liu et al. [4] | ✓ | CIM Unit | Sp. transformer infer. | Distribution Networks | Fixed | INT8 | Single | Bitmap | Med.
2023 | Flexagon[5] | ✗ | MAC PE Array | Sparse-Sparse Matmul | Merge-Reduce Trees | Flexible | INT16 | Dual | Indexed | High
2024 | Onyx[6] | ✓ | CGRA | General-purpose str. ops | Indirection, Inters., Union | Flexible | BF16, INT16 | Both | Indexed | High
[1] V. Dadu et al., MICRO ‘52, 2019
[2] E. Qin et al., IEEE HPCA, 2020
[3] W. Huang et al., IEEE VLSI, 2022
[4] S. Liu et al., IEEE ISSCC, 2023
[5] F. Muñoz-Martínez et al., ASPLOS, 2023
[6] K. Koul et al., IEEE VLSI, 2025

## Slide 10: Architecture: Background
Current SoftHier Architecture
  System Level
    Clusters in 2D-Mesh, HBM as main memory
    Clusters and HBM CTRL connected by NoC
  Compute Cluster
    RedMule Compute Engine
    Snitch – RISC-V Core
    TCDM Multi-banked L1
    iDMA Engine
  Compute Engine
    Reduced-precision Matrix Multiplication Engine
    Mix-precision floating-point arithmetic (FP16/FP8)
    2D array of Compute Elements (CEs) arranged in Systolic-like structure
Core 0
Core 0
…
Core n
Comp. Engine
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To Data NoC Router
To Sync NoC Router
Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router

## Slide 11: Architecture: Initial Ideas
Build on SoftHier project
Extend architecture to improve LLM inference
  Quantization to low precisions
    Microscaling-like block quantization
  Sparsity support at multiple levels
    Block level: sparse quantized blocks
    Tile level: sparse L1 streamers
    NoC level: packing of narrow requests on wide NoC, coalescing at HBM endpoints
  Processing near memory
    Offload operations to HBM endpoints to reduce data movement costs
Core 0
Core 0
…
Core n
Compute Engine
iDMA
I $
TCDM (Multi-banked L1)
CTRL
REG
Interconnect
To Data NoC Router
To Sync NoC Router
TE Cluster
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
HBM
HBM
HBM
HBM
R
R
Data NoC Router
Sync NoC Router
R
R
HBM
Compute Engine
Compute Engine
iDMA
TCDM (Multi-banked L1)
Interconnect
HBM

## Slide 12: Architecture: Quantization
Microscaling-like[1] FP block quantization
  Quantize elements to low precision (e.g. FP4, FP6)
  Form blocks with shared scale factor (e.g. 8 bit)
Quantization handled in compute engine
  Extend engine to process quantized blocks
  Maximize datapath reuse between formats & operations
Customize block formats to add sparsity
  Use small blocks (e.g. 64 bit) to minimize structure constraints
  Add metadata to encode block-level sparsity
[1] B. D. Rouhani et al., “OCP Microscaling Formats (MX) Specification,” OCP
6 × FP8
8 × FP6
12 × FP4
scale
sp.
scale
sp.
scale
spars.
48b elements
16b scale + sparsity

## Slide 13: Architecture: Sparsity in Compute Tile
Block level: extend quantized FP blocks with fine-grain sparsity
  Store lightweight sparsity encoding using additional small field in FP blocks
  N:M positional encoding, bit mask, or other low-overhead scheme
Tile level: sparse streaming units (SUs)
  Affine or indirect (scatter-gather) streaming of blocks for unstructured sparsity[1]
  Use indices (8b, 16b) residing in TCDM
  Possibly: index intersection or union between SUs for sparse-sparse workloads
Compute Engine
…
e0
e1
…
e7
shared scale
sparse enc.
0
6
42
48
56
sparse block B
dense block A
SU 1
idx comp.
SU 0
addrgen
addrgen
SU 2
addrgen
TCDM (Multi-banked L1)
Compute Engine
idcs
data
[1] P. Scheffler et al., “Sparse Stream Semantic Registers: A Lightweight ISA Extension Accelerating General Sparse Linear Algebra,” IEEE TPDS, 2023

## Slide 14: Architecture: Sparsity at NoC Level
Structured sparsity limits LLMs
  Better performance and size achievable[1]
  Needs system-wide unstructured sparsity
Problem: unstructured sparsity incurs non-contiguous accesses
  NoC and HBMx granularity (256b) much wider than data  low bandwidth utilization
  HBM endpoints are distributed
Pack narrow accesses on NoC bus
  Clusters pack together accesses per endpoint to improve NoC efficiency
  HBM endpoints unpack and coalesce accesses to maximize bandwidth
How can I use more of my links’ BW?
Cluster
HBM0
HBM1
HBM2
HBM3
…
…
…
…
Cluster
64b
64b
64b
64b
…
HBM Endpoint
wide NoC bus
…
unused BW
Cluster
request packer
64b
64b
64b
64b
64b
64b
64b
64b
64b
64b
64b
64b
64b
64b
HBM Endpoint
coalescer
NoC Router
…
…
64b
[1] S. Liu et al., “Ten Lessons We Have Learned in the New ‘Sparseland’:
A Short Handbook for Sparse Neural Network Researchers,” ICLR 2023

## Slide 15: Architecture: Processing Near Memory
Avoid data movement to compute cluster for simple operations
  Element-wise operators
  Simple reductions (e.g. dot products)
  Data reorganization (e.g. transposition)
Extend HBM endpoints with simple compute capabilities
  Extend NoC requests with special compute instructions
  Response carries result or merely signals operation completion
Reserve cluster compute and BW for more complex tasks
Cluster
NoC Router
HBM Endpoint
Near-Memory Compute Unit
Access Coalescer
HBM Controller
PNM controller
Instr. + args
Resp. (return)

## Slide 16: Block-level Design and Evaluation
Model critical hardware blocks as:
  Synthesizable RTL description
Analyze block-level PPA using RTL
  Profile in cycle-accurate simulation
  Estimate power & area based on logic synthesis and backend (P&R)
Use GVSoC for in-system simulation
  System simulator (GVSoC) model
  Calibrate using RTL findings
  Evaluate block designs based on application performance
Use findings to iterate on designs
Block design
RTL model
GVSoC model
refine
Block
Perf. & Power
Block Area
implement
simulate
In-System Perf. & Power
simulate
calibrate

## Slide 17: System-level Design and Evaluation
GVSoC[1]: Fast and Accurate Full-Platform Simulator
  Provide accurate timing (<10% runtime deviation vs. FPGA emulation of PULP IPs)
  Fast simulation (25 MIPS measured with a 16-core PULP Cluster)
System Calibration
  Block-level models integration
  Calibrate simulator using RTL-level block findings
Larger workload evaluation
  Use GVSoC to evaluate architecture design with end-to-end applications at fast simulation time
GVSoC
[1] Bruschi, Nazareno, et al. "GVSoC: a highly configurable, fast and accurate full-platform simulator for RISC-V based IoT processors." ICCD 2021.

## Slide 18: LLM Network Mapping
Explore mapping configuration space
  Single-chiplet dimensioning and workload distribution
  Data mapping in 3D-stacked memories and data exchange within the multi-level memory hierarchy
  Scaling to multi-chiplet
Flexible Model Mapping with Standardized High-Level Specifications
  Neural network compiler generates hardware-specific bare-metal C code
  Ingesting quantized ONNX graph specification
  Workload scheduling and tiling w.r.t. multi-level memory constraints

## Slide 19: Tuning for SoA LLM Workload
Architectural evaluation on full real-world workloads
  Leverage on GVSoC hardware abstract models and neural network compiler for fast benchmarking
  Evaluate performance, energy efficiency, and scalability
  Make adaptations to improve performance and efficiency by tuning and benchmarking a collection of models
Extend models to emerging technologies
  NV memories, 3D-DRAM with vertical transistors, and HBM4 with 3D-stacked memories
Tracking the evolution of advance AI models