## Slide 1: SoftHier Bi-Weekly Meeting
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 2
SoftHier Progress General Updates
FlooNoC RTL Updates
  Support collective operations {Multicast + Reduction}
  Reduction operation implementation: reuse FPUs of snitch cores
  Performance analyze
  Calibrate with GVSoC NoC models
Absence Announcement
  Chi will take holiday from 22nd Aug to 12nd Sep

## Slide 3
Reduction on FlooNoC
Reduction Extension in Router
  Flit extension: Add tag in flit head {OffloadRed, RedOp}
  Router Extension:
    FSM extension and export offload ports to Snitch FPUs
    Execute Reduction in a SIMD way
    Pipelined scheduling for best performance
Pack & Unpack
FPU
FPU
FPU
FPU
FPU
FPU
FPU
FPU
Operand1
512b
Operand2
512b
Result
512b
Optype
/64
/64
/64
/64
/64
/64
/64
/64
Router

## Slide 4
Example: Row-wise Red.Sum in FlatAttention
In RTL Implementation
  Row-wise Reduction can be fully pipelined
Router3
L1
FPU
Router2
Router1
Router0
L1
FPU
L1
FPU
L1
FPU
FPU Latency
Hop Latency
FPU Latency
Hop Latency
FPU Latency
Fully Pipelined

## Slide 5
GVSoC Calibration: Row-wise Red.Sum
Calibration
  Average Runtime cycle deviation is around 16%
  In RTL the DMA generate intervals per 4KB (AXI Page Size) transfer
  Fine-tune the GVSoC model for better accuracy
Chart: Calibration: Row-wise Red.Sum on NoC
| 2 | 3 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
RTL | 86 | 107 | 125 | 189 | 261 | 331 | 403 | 467 | 539 | 613
GVSoC | 61 | 79 | 97 | 161 | 225 | 289 | 353 | 417 | 481 | 545
Deviation(%) | 0.2907 | 0.26168 | 0.224 | 0.14815 | 0.13793 | 0.12689 | 0.12407 | 0.10707 | 0.10761 | 0.11093

## Slide 6
Performance Bottleneck: Router Reduce with >2 inputs
When the reduction path is not on a single chain
  For example: reduce from all clusters
    Tree-based reduction path
  Routers on the merge node need to reduce >2 inputs of flits
  Since we did not implement with more FPUs in place (would be very expensive)
  Introducing more stalls due to reduction dependency
  We are adding these details also in GVSoC model
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
R
A[i]
B[i]
C[i]
D[i]

## Slide 7
Plan For Next
Analyze Power and Area for FlooNoC with Collective Extensions
As this project approaches its conclusion, we need to allocate time to finalize the report and the open-source code for release {GVSoC, RTL}.