## Slide 1: SoftHier Bi-Weekly Meeting
Chi Zhang chizhang@iis.ee.ethz.ch
Thomas Benz tbenz@iis.ee.ethz.ch
Luca Colagrande colluca@iis.ee.ethz.ch

## Slide 2
SoftHier Progress General Updates
Working on the Flatten-Attention Paper (Chi, Luca C, Thomas etc.)
  Target ISVLSI, DDL Feb 10
More features supported on SoftHier simulator
  HBM Preloading:
    Python Numpy data array -> SoftHier HBM
    Can specify different base address for different Numpy arrays
  Partial cluster synchronization
    Now support grouping cluster in mesh shape
  Simple collective primitives on NoC model
    Row/column-wise multicast/reduction
  Introduce Spatz model (vector engine)
    ISA: RISCV vector extension, offloaded from snitch core
    Only vector instruction included for Flatten Attention are timed

## Slide 3
Optimization for Flatten Attention Dataflow
Optimization
  Using asynchronization nature of iDMA and RedMule invoking
  One cluster dealing with 2 heads concurrently
  Overlap the runtime of {iDMA, RedMule, Spatz}
Original
Optimized

## Slide 4
SoftHier + Flatten Attention wins
Directly compare with H100 + FlashAttention-3
  SoftHier configuration
    32x32 Cluster, 16x2 HBM ch, 1024b NoC link width
    Each Cluster: {RedMule 32x16 (1TFLOPS), Spatz FP16(64GFLOPS), 328KB L1, 512GB/s L1 BW}

## Slide 5
Next Steps
Focus on Flatten-Attention Paper
  DDL in 2 weeks